## Slide 1
Can AI make a robot dance to music?
Human dance generation is expressive; humanoid execution is constrained by physics.
SHOWCASE
looks like dancing
FREE-ROOT
tests physical survival
Key question: not only "does it move?", but "can it stand?"

## Slide 2
The missing link
BACKGROUND | MUSIC-TO-DANCE VS ROBOT EXECUTION
Music-to-Dance
EDGE / AIST++ / Bailando
Generates human skeleton or SMPL motion. Great for visual choreography, not robot dynamics.
Robot Dance
MoCap / choreography / MPC / RL
Can execute designed motions, but usually not direct arbitrary music-conditioned generation.
Our focus
Physics-aware retargeting from music-conditioned human dance to Unitree G1 rollout.
Direct music → stable humanoid dance is not yet an off-the-shelf solution.

## Slide 3
Project goal and innovation
POSITIONING | A PHYSICS-AWARE BRIDGE
Input
Music / existing generated pkl SMPL human dance motion
Our contribution
Retarget
SMPL-to-G1 mapping and diagnostics
Constrain
safe / expressive / balance / showcase profiles
Evaluate
pinned visual check + free-root physics rollout
Output
PINNED
visual showcase
FREE-ROOT
stable rollout
Innovation: an honest bridge and evaluation framework, not just a video demo.

## Slide 4
Pipeline: retarget, constrain, simulate
METHOD | FROM SMPL DANCE TO G1 ROLLOUT
01
Music / pkl motion
Generated or existing dance clips.
02
SMPL human dance
Human motion prior from music models.
03
SMPL-to-G1 retargeting
Map body parts and adapt arms.
04
Motion profiles
Safe, expressive, balance, showcase.
05
MuJoCo PD rollout
Pinned display or free-root validation.
Contact-aware balance correction + support-foot locking for the free-root branch

## Slide 5
Experimental setup
EVALUATION | WHAT WE TESTED
ROBOT
Unitree G1 in MuJoCo
CONTROLLER
PD tracking
MOTION CLIPS
Pop-style generated motion + AIST++ Waack
MODES
Pinned-root showcase vs free-root rollout
METRICS
Stability, fall time, pelvis height, amplitude, foot slip
Pinned showcase
Fixed root Best visual expressiveness Not a physical proof
Free-root stable
Floating root Normal gravity simulation Physical stability check
This separation avoids overclaiming: visual quality and physical validity are different questions.

## Slide 6
Results: expressive motions fall, stable motions shrink
ANALYSIS | STABILITY–EXPRESSIVENESS TRADE-OFF
Expressive free-root
can fall early
Contact-aware / footlock
100% stable on tested clips
Pinned showcase
best visual dance quality
Foot slip
small reduction after lock
Pinned answers: does it look like dancing? Free-root answers: can it physically survive?

## Slide 7
Takeaways and next steps
CONCLUSION | WHAT WE LEARNED
Key takeaways
Human dance is not robot motion
Music-to-dance output still needs robot-aware processing.
Trade-off is central
Expressiveness and free-root stability pull in opposite directions.
Two outputs are honest
Showcase for visual quality; free-root rollout for physics.
Future work
- Contact-aware lower-body IK - COM-aware root correction - Better support-phase detection - Learning-based policy tracking - More music styles and longer clips
Next goal: not only keep G1 standing, but preserve dance expressiveness under real physical constraints.